## Slide 1
A practical guide
mbowry@triumf.ca
M. Bowry, 8th February 2019
Experimental measurements of gamma-ray angular correlations with GRIFFIN

## Slide 2
Recommended reading
mbowry@triumf.ca
The GRIFFIN facility for Decay-Spectroscopy studies at TRIUMF-ISAC, Nuclear Inst. and Methods in Physics Research A, 918, 9 (2019)
Gamma-gamma angular correlation techniques with the GRIFFIN spectrometer, Nuclear Inst. and Methods in Physics Research A, 922, 47 (2019)
M1-E2 mixing ratios and conversion electron particle parameters for the electromagnetic transitions in 75As, Physical Review 180, 1043 (1969)
Nuclear Physics of Stars Appendix D, C. Iliadis, pg. 599-617
(Report) Compton Polarimetry with GRIFFIN Documentation and Physics Review,
  Plone: Griffin->Reports->Co-op Report, Dan Southall

## Slide 3
Introduction
mbowry@triumf.ca
=
Rate per crystal reflects angular distribution
Angular distribution of radiation emitted in decay experiments
  Ensemble of “orientated” radioactive nuclei decay from state (i.e. nuclei orientated with unequal population of magnetic sub-states), aligned with respect to experiment
detectors

## Slide 4
Introduction
mbowry@triumf.ca
Angular distribution of radiation emitted in decay experiments
  Ensemble of radioactive nuclei with no preferred orientation (in decay, no gate on outgoing particle or not detected at all) and no alignment relative to the experiment.
=
Rate per crystal is isotropic
=
detectors

## Slide 5
Introduction
mbowry@triumf.ca
Angular correlation: measure the coincidence frequency of two successive decays at different angles ( orientated with respect to )
=
Rate provides angular correlation
=
X
detectors

## Slide 6
Introduction
mbowry@triumf.ca
Angular correlation formula (generalized)
where:
,
,
.. simplifies to a short expansion for many γ-γ cascades (L=1,2).

## Slide 7
Introduction
mbowry@triumf.ca
Quality factors
  In general, the measured angular correlation does not represent nature exactly: is highly sensitive to the experimental setup and other factors including:
    Non-negligible lifetimes of intermediate nuclear states ()
    Detector size, geometry and efficiency.
  For a complex setup like GRIFFIN, simulations provide the most direct route to extracting accurate measurements (of for example).
J.K. Smith et al.

## Slide 8
Analysis procedure
mbowry@triumf.ca
Unpack data using GRSISort (MIDAS fragments  ROOT trees)
Sort data using GRSI-Parallel ROOT Facility (i.e. parallelized analysis)
Go to .. /GRSISort/GRSIProof/
PROOF scripts have two parts, a header (.h) and main (.C)
  > cp AngularCorrelationSelector.C ggAngularCorrelation.C
  > cp AngularCorrelationSelector.h ggAngularCorrelation.h
  Open the new files in a text editor (e.g. vim, gedit etc.).
  Replace references to these new names within each file.
See also slides by R. Dunlop available online (Plone):
  https://grsi.wiki.triumf.ca/index.php/Access
  Follow link to Plone page (requires registration)
  General->Meetings->Joint Tigress and Griffin Collaboration Meeting 2017->GRSISort presentations

## Slide 9
Setting up GRSIPROOF
mbowry@triumf.ca
Currently, ggAngularCorrelation is setup to automatically generate γ-γ coincidence angles using spatial coordinates stored in the TGriffin library.
  ../GRSISort/libraries/TGRSIAnalysis/TGriffin/TGriffin.cxx
Theta, °
Phi, °

## Slide 10
Setting up GRSIPROOF
mbowry@triumf.ca
Both ROOT and GRSI-specific functions are employed in ggAngularCorrelation.h to return the available coincidence angles.
Function definition
Body
Detector modifications (etc.) go here!

## Slide 11
Setting up GRSIPROOF
mbowry@triumf.ca
Histograms are defined in ggAngularCorrelation.C where the general format is:
Histogram definitions
Body
#define ggAngularCorrelation_cxx
#include “ggAngularCorrelation.h”
//variable definitions (doubles, integers etc.)
void ggAngularCorrelation::CreateHistograms() { ; }
void ggAngularCorrelation::FillHistograms() { ; }

## Slide 12
Setting up GRSIPROOF
mbowry@triumf.ca
Modify the .C file to suit the task.
  Remove histograms that will not be used (including Create.. and Fill.. functions). Additional histograms mean more memory usage multiplied by the number of parallel threads!
  Check histogram binning (more bins = more memory usage).
  Add event-mixing depth functionality. This is used to reduce the statistical uncertainty in the event-mixed coincidence spectra and is simple to implement.
  Add diagnostic spectra to check angle calculations are functioning normally (always assume your code is broken from the beginning).
“gammaGamma”, “gammaGammaBG”, “gammaGammaMixed” ☺
( + diagnostic histograms)
Single-crystal analysis (no addback)

## Slide 13
Setting up GRSIPROOF
mbowry@triumf.ca
Gamma-gamma angular correlation matrices (ggAngularCorrelation.C)

## Slide 14
Setting up GRSIPROOF
mbowry@triumf.ca
Gamma-gamma angular correlation matrices + event mixing

## Slide 15
Setting up GRSIPROOF
mbowry@triumf.ca
Add diagnostic histograms. This includes the basics (hit energy summed over the whole array, time difference etc.) in addition to ensuring:
  The calculated angles are accurate
  The correct (grouped) angles are assigned to the appropriate bins.
For example, the relative change in the integral (or the counts in a given photopeak) of the event-mixed matrices will be very similar to the relative combinatorial weights (# crystal pairs) and is easily checked.

## Slide 16
Setting up GRSIPROOF
mbowry@triumf.ca
In this example analysis, the number of angles is restricted to 7 (full analysis = 51 angle bins).
Added filter to Create and Fill functions to exclude other angles. This is useful for any analysis to reduce the number of histograms.
Filter can be modified to include the next set of angles etc.
Issues encountered with ROOT v6.06.08 + GRSISort v3.1.3.4 regarding the angleIndex iterator (solution available). Use GRSISort v3.1.3.5 or higher.
Index number: {0, 4, 10, 25, 40, 46, 50}
Angle (°): {18.8, 33.7, 60.2, 91.5, 126.2, 148.1, 180.0}

## Slide 17
Setting up GRSIPROOF
mbowry@triumf.ca
Run PROOF. For example, in a terminal within a /data/ directory:
Common failure modes. All of the following will cause a crash:
  Histogram definition missing in CreateHistograms function.
  Referencing hits in a detector branch that does not exist in the AnalysisTree or is not defined in the header file.
  Iterating over a value or object (e.g. a histogram) that does not exist. Most commonly occurs in a for(){ ; } loop.
Calibration files cannot be entered as a PROOF argument (yet).
PROOF compiled upon execution.
> grsiproof /path2/analysis09636* /path2/ggAngularCorrelation.C --max-workers=4

## Slide 18
Setting up GRSIPROOF
mbowry@triumf.ca
Running PROOF with the default number of workers
Most GRSI cluster machines have (effectively) 8 CPUs. The default number of workers is 8. To stop these processes:
> ps aux | grep proofserv
> kill -9 [pid1] [pid2] .. [pidN]
Reduce the number of workers, histograms or histogram binning and try again (e.g. add angle filter).
Your PC

## Slide 19
Results and analysis
mbowry@triumf.ca
Hit energy summed over the array (Eu-152 decay)
Your PC
After gainmatching + calibration
Before gainmatching + calibration
122
245
344
X rays

## Slide 20
Results and analysis
mbowry@triumf.ca
Time difference (between any two HPGe crystals)
  Scale factor for time-random subtraction = (500/1000) = 0.5
Your PC
Time Random
Prompt

## Slide 21
Results and analysis
mbowry@triumf.ca
Relative integrals: Event-mixed γγ matrices
Your PC

## Slide 22
Results and Analysis
mbowry@triumf.ca
Time-random (TR) subtractions
Note: TR subtractions not required for event-mixed γγ matrices
Also available: James Smallcombe’s jRoot environment for gating and peak fitting (added functionality w.r.t. TBGSubtraction): https://github.com/jsmallcombe/jRootAnalysisTools
> grsisort
> gammaGammaBG[i]->Scale(500./1000.);
> gammaGamma0->Add(gammaGammaBG[i],-1.);
> new TBGSubtraction(gammaGamma0);

## Slide 23
Results and Analysis
mbowry@triumf.ca
Gating
Control peak and background gates
Save spectra
Fit Peak

## Slide 24
Results and Analysis
mbowry@triumf.ca
Peak fitting
Control over peak parameters most useful
Background and high-energy tail* have a significant effect on the success/failure of the fit.
*e.g. due to poor gainmatching, pile-up
Reduced chi-squared values, 18.8 to 180.0°
Correlated : {3.00, 3.07, 1.87, 1.50, 5.30, 2.24, 2.12}
Event-mixed : {3.25, 1.77, 1.93, 2.91, 4.80, 2.90, 1.64}
7,000  20,000 counts in the correlated peaks.
.. always room for improvement!
Event-mixed peak fit, modified TPeak,
ChiSq = 2.91

## Slide 25
Results and Analysis
mbowry@triumf.ca
Angular correlation
3 days later …

## Slide 26
Results and Analysis
mbowry@triumf.ca
Angular correlation
3 days later …

## Slide 27
Results and Analysis
mbowry@triumf.ca
Angular correlation, reverse gate (fit the 1408)
3 days later …